Oklahoma N-Rail Stacker End Plates

Note in the above diagram that there are two 3/8” holes 8” from the front and back and 1.75” above the bottom of the frame, with a 3/8: tee nut inserted on the inside. These are for the end plates used by Oklahoma N-Rail for transporting the modules.  As shown in the diagram below, the end plate for a straight module is an 17” X 24” piece of 1/2” plywood.  It has two 3/8” holes drilled in the same location as the end boards of the module frame.  The end plate has a 3” X 8” rectangular hole for use as a handhold.  It has three 1X2 (3/4” by 1 1/2”) boards glued and screwed with drywall screws to the plywood.  One 24” long 1X2 is fastened to the inside upper edge of the plywood as shown in the side view below.  The other two are fastened diagonally to the outside of the plywood as shown in the front view.  These boards normally extend an inch or two above and below the plywood, unless they are intended to be used for the bottom or top module in a stack of modules.  The diagonal board should not extend below the bottom of the plywood for the bottom module, or above the top of the plywood for the top module.  The end plates for a straight module are attached by two 1 3/4” long (including hex head) 3/8” machine screws with a washer.

# Text boxes

17”

1.75”

6”

3”

8.5”

8”

7.5”

8”

13.5”

5.75”

4.5”

40”

3”

3”

3”

3”

12”

8”

8”

8”

1.75”

5”

5”

14”

13.5”

5.25”

5.25”

4.75”

8”

8”

8”

8”

3”

6”

1.75”

17”

14”

5.5”

4.5”

9.5”

9.5”

8”

1.75”

6”

3”

17”

8”

24”

8”

24”

22”

24”

24”

8”

8”

24”

17”

1.75”

6”

3”

8”

24”

22”

24”

17”

1.75”

6”

3”

7.5”

8”

8.5”

8”

13.5”

4.75”

5.75”

14”

4.5”

5.5”